## Slide 1
Deep Optimizations of CNNs and Efficient Deployment on IoT Devices
Bharath Sudharsan and Pankesh Patel

## Slide 2
Neural Networks on IoT Devices
TinyML is ultra-low-power machine learning. Basically running NNs on MCUs. We categorize TinyML app landscape into
  Audio-based always-on ML inference for context recognition, spot keywords/wake-words/control-words
  Industry telemetry data-based use cases where models deployed on MCUs monitor IMUs, motor bearing vibrations, or other sensors to detect anomalies and predict equipment faults
  Image data-based use cases such as object counting, text recognition, visual wake words
  Physiological/behavior data-based use cases such as activity recognition using IMU or EMG data
Notes: https://cms.tinyml.org/wp-content/uploads/summit2021/tinyMLSummit2021d3_Partner3_Carlson.pdf

## Slide 3
Neural Networks on IoT Devices
Who are practicing TinyML: Executing NNs on their MCU-based products
Notes: https://scholar.harvard.edu/files/vijay-janapa-reddi/files/tinymlsummit2020-4-4-janapareddi_01.pdf

## Slide 4
Challenges in Prevailing Approaches
Existing Programming Frameworks
  Compression levels, speedups produced by generic optimization toolkits in ML frameworks (e.g., PyTorch, Tensorflow) are not sufficient since they target are targeted for smartphones and better-resourced IoT hardware such as Raspberry Pis, Jetson Nano
  The early-stage TF Lite for Microcontrollers core runtime can fit in 16 KB on an Arm Cortex M3 and run basic NNs on MCUs without needing operating system support or dynamic memory allocation
  Still, to highly reduce the NN size before deploying and executing on MCUs using TF Micro, there is a need to optimize high memory, computation demanding models in multiple aspects to produce small size, low latency, low-power consuming models that can comfortably fit and execute on resource-constrained MCU-based IoT hardware

## Slide 5
Challenges in Prevailing Approaches
Performance Metrics Trade-offs
  During on-board model execution, an IoT application that interacts with the loaded model may demand high performance on a particular metric over others
  For example, a real-time IoT device would require ultra-fast inference, while a low-memory device would require the highest model size reduction
  So, the challenge is how to perform optimization that favors particular metrics over others?

## Slide 6
Challenges in Prevailing Approaches
Optimization Compatibility
  NNs optimized using one state-of-the-art method may exceed the target IoT device hardware's memory capacity by just a few bytes
  Need to spend days on unproductive to find a compatible optimizer, then implement it to check if the new compression and accuracy levels are satisfactory
  Models cannot be optimized further if failed to find a method that matches the previous optimizer. So, either have to tune the model network architecture and re-train from scratch
  To speed up the R&D phase (going from idea to product) of AI-powered IoT devices, we need a comprehensive guideline to optimize NN models that can readily be deployed on resource-constrained MCUs-based hardware

## Slide 7
Top Deep Optimization of NNs
Three-stage compression pipeline paper with Pruning + Quantization + Huffman coding
  Pruning reduces the number of weights by 10×. Quantization further improves the compression rate between 27× and 31×
  Huffman coding gives more compression between 35× and 49x. The compression scheme doesn’t incur any accuracy loss
Notes: https://arxiv.org/pdf/1510.00149)

## Slide 8
Top Deep Optimization of NNs
Once for all paper
  A single network is trained to support versatile architectural configurations including depth, width, kernel size, and resolution
  Given a deployment scenario, a specialized subnetwork is directly selected from the once-for-all network without training
  This approach reduces the cost of specialized deep learning deployment from O(N) to O(1)
Notes: https://arxiv.org/pdf/1908.09791.pdf

## Slide 9
Top Deep Optimization of NNs
MCUNet paper:
  TinyEngine achieves higher inference efficiency while reducing the memory usage. 3× and 1.6× faster than TF-Lite Micro (Google) and CMSIS-NN (ARM) respectively
  By reducing the memory usage TinyEngine can run various model designs with tiny memory, enlarging the design space for TinyNAS under the limited memory of MCU
  Outperforms existing libraries by eliminating runtime overheads, specializing each optimization technique, and adopting in-place depth-wise convolution
Notes: https://arxiv.org/pdf/2007.10319.pdf

## Slide 10
Research Question
Is it possible to combine more than one state-of-the-art optimization technique to achieve deeper compression levels of ML models? If possible, what is the maximum achievable size-reduction, inference speedup, and which combination shows the highest accuracy preservation?

## Slide 11
Multi-component NN Optimizer: Architecture
The architecture of our multi-component model optimizer
Sequence to follow for optimizing Neural Networks to enable its execution on resource-constrained AIoT boards, small CPUs, MCUs based IoT devices
In the upcoming slides each optimizer component shall be presented

## Slide 12
Use-case based NNs: Input
The optimizer takes a NN as an input and produces a highly optimized version of the input NN that can run on low resource, cost and power MCU-based IoT hardware. The input network can be
  Pre-trained models such as Inception, Xception, Mobilenet, Tiny-YOLO, Resnet, etc
  Or the custom-designed, yet to be trained networks

## Slide 13
Pre-training Optimization
The custom-designed, yet to be trained networks should pass through the pre-training optimization component
  Pruning: We implemented the magnitude-based weight pruning, where the model's weights are gradually zeroed out during the training to achieve model sparsity. Thus obtained sparse models are easier to compress, and the zeroes can be skipped during inference, resulting in latency improvements
  Quantization-aware Training: When quantizing a CNN, the parameters and computations go from a higher to lower precision, resulting in improved execution efficiency at a cost of information loss. This loss is because the model weights can only take a small set of values, thus losing the minute differences between them. To reduce the loss and maintain the model accuracy, we introduce quantization error as noise during the model training, as part of the overall loss, which the optimization algorithm in use tries to minimize

## Slide 14
Post-training Optimization
Quantizes the models by reducing the precision of their weights and activations to save memory and simplify calculations often without much impact on accuracy. Following are the popular techniques we implemented
  Int with float fallback quantization: Fully integer quantize a model, but use float operators when they don't have an integer implementation (to ensure conversion occurs smoothly)
  Float 16 quantization: Reduce the size of floating point models by quantizing the weights to IEEE standard for 16-bit floating point numbers. Float16 models run on small CPUs without modification
  Integer-only quantization: To improve the NN compatibility with integer only hardware devices or accelerators by making sure all model math is in integer

## Slide 15
Joint Pre and Post-training Optimization
First, any of the pre-training optimization methods has to be applied to the model, followed by its Int-8 post-training quantization
  When more than 11x size reduction is required
  Example, when we aim to execute Inception v3 (23.9 MB after quantization) on a AIoT boards, which only has only 16 MB Flash memory
+

## Slide 16
The interior of trained models is a graph with defined data flow patterns
  Graph contains an arrangement of nodes and edges
  Nodes represent the operations of a model
  Graph edges represent the flow of data between the nodes
We present techniques to optimize graphs of NN to improve the computational performance of NN while reducing peak SRAM usage on MCUs
We perform graph optimization in sequential steps
  Arithmetic Simplification
  Graph Structure Optimization
Graph Optimization

## Slide 17
Graph Optimization: Arithmetic simplification
Arithmetic re-writes rely on known inputs. As shown, the known constant vector is grouped with an unknown vector that might be constant or non-constant. After performing such re-writes, if the unknown vector turns out to be a constant, then graph performance improves

## Slide 18
Graph Optimization: Graph Structure
We propose tasks that when realized will optimize the graph for efficiency
  Task1: Remove loop-invariant sub-graphs. i.e., remove the loops that are true both before and after iterations.
  Task2: Remove dead branches/ends from the graphs. So, during execution on MCUs, backtracing from the dead-end is not required to progress in the graph.
  Task3: Use a transitive reduction algorithm on entire graph to remove redundant control edges. Shorten the critical path of a model step by rearranging control dependencies
  Task4: Replace recurrent subgraphs with optimized kernels/executable modules

## Slide 19
Graph Optimization: Graph Structure
Task5: This task when realized, reduces the graph's size resulting in processing speedups. Here, we identify and remove nodes that are effectively NoOps (a placeholder of control edges) and Identity nodes (outputs data with the same content and shape of input)

## Slide 20
Joint Graph and Post-Training Optimization
First, the two Arithmetic simplification and Graph Structure Optimization steps needs to be applied to the original un-optimized model
Then any of the post-training model optimizers need to be applied
+

## Slide 21
Operations Optimization
When designing ML models for tiny IoT hardware, only limited operations can be used to keep the cost low
Over 90% arithmetic operations are used by convolutional (CONV) layers. So, we already convert floating-point operations into int-8 (fixed point) during post-training quantization
Depth-separation of 3D filters
Also Decompose 2-D CONVs and 1-D CONVs to reduce parameters and operations count
3D convolution uses C * A * B multiplications, whereas a depth-separable 3D convolution only requires C + A + B multiplications

## Slide 22
Joint Operations & Post-training Optimization
Even if the models such as MobileNet and SqueezeNet are manually designed to execute within a tight memory budget, it would exceed the AIoT board's capacity by over 5 x times
Hence, we propose to first optimize the operations of any model, then perform post-training model optimization
+

## Slide 23
Workload Optimization
The complexity and size of the model have an impact on the workload
  Larger and denser models lead to increased processor workload
  Hardware spends more time working and less time idle resulting in elevated power consumption and heat output
We present techniques that can be used to reduce workloads. The methods we recommend apply globally, i.e., not biased towards local performance optimizations for a single operation, as in many previous works

## Slide 24
Workload Optimization
Input data reduction Use computationally inexpensive low pass filters
Hardware accelerators Resource-constrained devices are not capable to utilize off-the-shelf accelerators. For successful offloads, we recommend
  Storing the C code of the optimized model to be executed in a shared memory location
  Perform parallel offloading for internal data reuse
  Offload the processing to the inbuilt KPU, FFT units
Number of threads Limit the number of threads initialized by NNs for computation
Low-level optimization Perform low-level optimization of convolution to eliminate unnecessary data layout transformation overheads
Linear algebraic properties Analyze the linear algebraic properties of models and apply algorithms such as Strassen Gaussian elimination, Winograd's minimal ﬁltering

## Slide 25
Kernels Optimization
The general C/C++ implemented kernels for MCUs need hardware-specific optimizations
We present library independent kernel optimization techniques that are generic across a wide range of resource-constrained hardware for guaranteeing no runtime performance bottlenecks
  Remove excess modules, components in project directory before building a project
  Group multiple operators together within a single kernel
  Go deep into the assembly code level for improving small matrix multiplication tasks. Implement the matrix multiplication kernel with 2x2 kernels to save on load instructions
  Convolutions should be partitioned into disjoint pieces to achieve parallelism
  Self-customized thread pooling techniques should be used to reduce overheads while launching and suppressing threads to reduce performance jitters while adding threads

## Slide 26
RCE-NN Steps
Step1: Model to FlatBuffer Conversion
  Creates flat buffers of the CNNs
  Memory-mapped and can be utilized directly from disk/flash
  Zero additional memory requirements for data access

## Slide 27
RCE-NN Steps
Step2: FlatBuffer to C-byte Array
  MCUs in edge devices lack native filesystem support. Hence, we cannot load and execute the regular format (“.h5”, “.pb”, “.tflite”, etc.) trained CNNs
  We convert the quantized version of the trained model into a C array and compile it along with the program for the IoT application which is to be executed on the edge device
Translated C byte array:
unsigned char converted_quantised_model [] = {
0x18, 0x00, 0x00, 0x00, 0x54, 0x46, 0x4c, 0x33, 0x00, 0x00, 0x0e, 0x00,
...
...
…
};
unsigned int converted_quantised model_len = 21200;
Command: xxd -i converted_quantised_model file > translated c byte array of model.cc
Method to translate the trained model into a C byte array

## Slide 28
RCE-NN Steps
Step3: IoT App Integration
  We fuse the trained CNN (translated c-byte array) with the main program of an IoT use-case
  We build binaries that will be loaded on MCUs for execution
Step4: Deployment
  The generated binaries of a NN model are flashed via serial port on the MCU-based devices
  To flash, use an external In-System Programmer (ISP) or a ParallelProgrammer, which does not occupy bootloader space, also avoids the bootloader delay

## Slide 29
Resource-constrained IoT Hardware: Output
Output: A highly optimized version of the input NN that can run on low resource, cost and power IoT hardware such as the below shown MCUs

## Slide 30
Evaluation Setup
We implement each of the optimizer component on CNNs and present the experimental results
  We define a basic CNN whose architecture is shown below
  CNN1: When above network is trained using the standard MNIST Fashion dataset
  CNN2: When above network is trained using the MNIST Digits datasets

## Slide 31
Evaluation: Pre-training Optimization Components
Below, we show the architecture of the QAT CNN1
  2.49x smaller in size
  Can Infer 10.76 x times faster
The Pruned CNN1 architecture is same as the Original CNN1
  2.76x smaller in size
  Can Infer 1.85 x times faster

## Slide 32
Evaluation: Post-training Optimization Components
Below, we show the architecture of Int with float-fallback quantized CNN1
  12.06x smaller in size. Can Infer 960.85 x times faster
Below, we show the architecture of Float16 quantized CNN1
  6.31x smaller in size. Can Infer 1256.5 x times faster

## Slide 33
Evaluation: Post-training Optimization Components
Below, we show the architecture of Int-only quantized CNN1
  11.69x smaller in size. Can Infer 882.94 x times faster
Analyzing the post-training optimization results
  Float16 quantization for reasonable compression rates (we obtain approx. 6x compression), without loss of precision (we experience only 0.01 % loss in accuracy)
  Int with float-fallback quantization for smallest model size and fastest inference on MCUs
  Float16 quantization for fastest inference on CPUs

## Slide 34
Evaluation: Operation, Graph Optimization Components
Graph optimized CNN1: We implemented and performed all applicable arithmetic simplification rewrites and graph structure optimization tasks on CNNs
  2.76x smaller in size, 13.12x times faster
Below, we show the architecture of the Operations optimized CNN1
  6.36x times faster

## Slide 35
Optimization Results Analysis
We performed analysis based on the evaluation results
Best Optimization Sequence for Smallest Model Size:
  Graph optimized then integer with float fallback quantized version is only 22.5 KB
  12.06 x times smaller than original CNN
Best Optimization Sequence for Accuracy Preservation:
  Graph optimized then integer only quantized version
  For MNIST Fashion, the accuracy increased by 0.27 %, and by 0.13 % for MNIST Digits
Best Optimization Sequence for Fast Inference:
  Operations optimized then float16 quantized version
  Produces the fastest unit inference results in 0.06 ms

## Slide 36
Multi-component Optimizer Summary
To enable ultra-fast and accurate ML-based offline analytics on resource-constrained IoT devices, we present an end-to-end multi-component ML model optimization sequence
Researchers and developers can use our optimization sequence to optimize high memory, computation demanding models in multiple aspects in order to produce small size, low latency, low-power consuming models
Our optimization components can produce models that are; (i) 12.06 x times compressed; (ii) 0.13% to 0.27% more accurate; (iii) orders of magnitude faster unit inference at 0.06 ms

## Slide 37
Conclusion
To enable ultra-fast and accurate ML-based offline analytics on resource-constrained IoT devices, we presented an end-to-end multi-component ML model optimization sequence. Researchers and developers can use our optimization sequence to optimize high memory, computation demanding models in multiple aspects to produce small size, low latency, low-power consuming models

## Slide 38
Contact: Bharath Sudharsan
Email: bharath.sudharsan@insight-centre.org
www.confirm.ie
Notes: If you have any further queries you can contact us anytime.
Thank you, stay safe.